## Slide 1
CLIMBING

## Slide 2
OVERVIEW
Aim
Objectives
Revision
Definitions
Forces in a Climb
Types of Climb
Factors affecting Climb Performance
Application
Airmanship/Threat and Error Management
Revision Questions

## Slide 3
To understand the aerodynamic principles and practical applications how to correctly enter, maintain and exit a climb
AIM

## Slide 4
OBJECTIVES
Describe the interaction of the four forces during a climb
State the effect on climb rate and angle when subject the following factors:
  Weight
  Flaps
  Headwind/tailwind
  Power
  Density
State the procedure in entering, maintaining and exiting a climb
Identify threats associated with climbing the aircraft

## Slide 5
REVISION

## Slide 6
REVISION
State the four forces in straight and level flight. Which forces act equal to each other in order to achieve equilibrium?
Lift, Drag, Thrust and Weight
Lift = Weight Thrust = Drag
2. State the two types of drag
Induced and Parasite (Form, Skin Friction and Interference)
3. State the normal cruise configuration
4800 RPM, Four Fingers, 95 knots
4. State the Maintenance Cycle
Attitude, Lookout, Attitude, Performance

## Slide 7
DEFINITIONS

## Slide 8
DEFINITIONS
Best Rate of Climb (RoC) Vy: Highest vertical speed of the aeroplane in feet per minute (ft/min)
Best Angle of Climb (AoC) Vx: Highest vertical height in the shortest ground distance (ft/nm)
Power: Rate of doing work. Power = Thrust x Speed
Groundspeed: Speed of the aeroplane over the ground
Service Ceiling: Altitude at which the aircraft can only maintain a climb of 100ft/min
Absolute Ceiling: Altitude at which the aircraft can no longer climb

## Slide 9
DEFINITIONS
Vx
Vy
Best Angle of Climb
Best Rate of Climb
Distance traveled
Altitude gained
Vcrz
Elapsed Time is 1 minute

## Slide 10
PRINCIPLES
PRINCIPLES

## Slide 11
FORCES OF
STRAIGHT AND LEVEL
REVISION
COUPLED MOMENTS: Caused by the interaction of two moments connected by the horizontal distances, thus creating a twisting force.
Weight
Total Drag
Lift
Thrust
L/W couple
Horizontal stabilizer
down force
T/D couple
Horizontal stabilizer down force

## Slide 12
FORCES IN A STEADY CLIMB
PRINCIPLES
Total Drag
W1
RCW
In a climb:
L is less than W
Ta
L
W
Dt
Tr
Tr needs to overcome Total Drag
During a climb it’s the excess thrust which overcomes the W2 component of weight.
Te

## Slide 13
TYPES OF CLIMB
PRINCIPLES

## Slide 14
BEST ANGLE OF CLIMB
Best height to horizontal distance ratio
Occurs when maximum excess thrust occurs, the difference between thrust output and total drag
Primarily used for obstacle clearance after take-off
Poor forward visibility and poor engine cooling
SLG2 65 KNOTS
PRINCIPLES
THRUST
THRUST AVAILABLE
Vx
Vy
Cruise climb
Maximum excess thrust
THRUST REQUIRED
IAS

## Slide 15
BEST RATE OF CLIMB
Best height to time ratio
Occurs at maximum excess power
Primary used for take-off or if a quick climb is necessary
Slightly better forward visibility and engine cooling
SLG2 72 KNOTS
PRINCIPLES
Vx
Vy
Cruise Climb
POWER AVAILABLE
POWER REQUIRED
Maximum excess HP
IAS
HP

## Slide 16
CRUISE CLIMB
Compromise between rate and speed
Used for most climbs if best angle or rate is not essential
No defined speed in Flight Manual
Allows for engine cooling and provides good forward visibility
SLG2 85 KNOTS
PRINCIPLES

## Slide 17
TYPES OF CLIMB
Vx: 65 kts
Vy: 72 kts
Best Angle of Climb
Best Rate of Climb
Distance traveled
Altitude gained
Cruise Climb
V: 85 kts
Elapsed Time is 1 minute

## Slide 18
FACTORS AFFECTING CLIMB
FACTORS AND CONSIDERATIONS

## Slide 19
WEIGHT
FACTORS AND CONSIDERATIONS
Increased weight means lift must be increased to maintain the aircraft in a balanced condition.
Extra lift increases the drag, reducing the amount of excess thrust and power available.
Vx
Vy
Power available
Power required
Maximum excess HP
Vx
Vy
Cruise climb
Maximum excess thrust
Thrust required
Thrust available
IAS
IAS
HP
THRUST

## Slide 20
DENSITY
FACTORS AND CONSIDERATIONS
ALTITUDE
As altitude increases the outside air density decreases
Therefore, there is less power available, reducing climb performance.
Propeller becomes less efficient further reducing the thrust available
Vx
Vy
Cruise Climb
Power available
Power required
Maximum excess HP
Vx
Vy
Cruise climb
Maximum excess thrust
Thrust required
Thrust available
TEMPERATURE/HUMIDITY
Increasing either temperature or humidity also decreases the air density
Having the same effect on climb performance as increasing altitude
IAS
IAS
HP
THRUST

## Slide 21
WIND
FACTORS AND CONSIDERATIONS
At a constant airspeed the rate of climb is unaffected by wind. The angle of climb, however, is increased when climbing into a headwind and reduced when climbing into a tailwind.
500ft
For the same airspeed and power, all three aeroplanes reach this height in the same time interval
NIL WIND
HEADWIND
TAILDWIND

## Slide 22
FLAPS
Used in take-off to produce a large lift force with an additional small drag force
Reduces take off distance required however reduces both angle of climb and rate of climb
FACTORS AND CONSIDERATIONS

## Slide 23
POWER
Decrease in power
Decrease in angle of climb
Decrease in rate of climb
NOTE: all climbs in SLG2 are done at full throttle
FACTORS AND CONSIDERATIONS
Vx
Vy
Cruise Climb
Power available
Power required
Maximum excess HP
IAS
HP

## Slide 24
SUMMARY
FACTOR | RATE OF CLIMB | ANGLE OF CLIMB
INCREASE POWER |  | 
DECREASE DENSITY INCREASE HEIGHT |  | 
INCREASE WEIGHT |  | 
HEADWIND |  | 
TAILWIND |  | 
DEPLOY FLAPS |  | 
FACTORS AND CONSIDERATIONS

## Slide 25
APPLICATION

## Slide 26
PRE ENTRY CHECKS
Heading SELECT HEADING (HDG)
Altitude SELECT ALTITUDE (ALT)
Lookout
APPLICATION

## Slide 27
Power FULL THROTTLE
Attitude SET as required
Speed Wait for speed to stabilise
Trim TRIM the aircraft
Increase in power causes a yaw left
Step on the right rudder pedal to prevent yaw
APPLICATION
Entry

## Slide 28
ATTITUDE
LOOKOUT
ATTITUDE
PERFORMANCE
LOOKCOOL Checks
Every 1000 feet, lower the nose for lookout and cool the engine
APPLICATION
Work Cycle

## Slide 29
APPLICATION
Performance

## Slide 30
PERFORMANCE
APPLICATION

## Slide 31
BALANCE
AIRCRAFT SHOULD ALWAYS BE BALANCED
APPLICATION

## Slide 32
Attitude Set the attitude
Speed Allow the speed to increase to required speed
Power Reduce power back to cruise
Trim Trim aircraft for ‘hands off’
Anticipate level off by 10%
APPLICATION
APPLICATION
Levelling Off

## Slide 33
APPLICATION
Pre-entry
Choose reference point
Heading
Altitude
Lookout
Power
Attitude
Speed
Trim
Attitude
Speed
Power
Trim
Attitude Lookout Attitude Performance

## Slide 34
PAST | Best Angle Climb | Best Rate Climb | Cruise Climb
Power | FULL | FULL | FULL
Attitude | Cowling four fingers above the horizon | Cowling two fingers above horizon | Cowling on horizon
Speed | 65 knots | 72 knots | 85 knots
Trim | TRIM for Hands Off State |  | 
POWER SETTINGS
APPLICATION

## Slide 35
AIRMANSHIP
LOOKOUT: Maintain proper lookout (clock code)
WORK CYCLE: Maintain a constant and correct work cycle
CONTROL HANDLING: Smooth applications on the controls and throttle
Handover & Takeover Procedures: Verbalise
TRIM: Make sure you trim the aircraft

## Slide 36
THREAT | ERROR | MANAGEMENT
THREAT AND ERROR MANAGEMENT
Reduced forward visibility
Improper use of maintenance cycle
LOOKCOOL procedure
Overstressing the engine
Rough handling of throttle
Smooth applications
Stalling
Pulling back on the control stick too much and not checking airspeed
Maintain speed during climb

## Slide 37
REVISION QUESTIONS
Describe the interaction of the four forces during a climb
State the effect on climb rate and angle when subject the following factors:
  Weight
  Flaps
  Headwind/tailwind
  Power
  Density
State the procedure in entering, maintaining and exiting a climb
Identify threats associated with climbing the aircraft